## Slide 1: UNIT: Oxy-Fuel Welding, Brazing, Cutting and Heating
LESSON: OXY-ACETYLENE EQUIPMENT SAFETY
Standard B7.2 – Know how to properly set up, adjust, shut down and maintain an oxy-fuel system
Notes: <number>

## Slide 2: OXY-FUEL UNIT Identification
Oxygen Regulator
Acetylene Regulator
Oxy-Acetylene Hoses
Oxy-Acetylene Cart
Oxygen Cylinder Valve
Oxygen Cylinder
Acetylene Cylinder Valve
Acetylene Cylinder
Cylinder Safety Chain

## Slide 3: SECURING THE CYLINDER
Always chain or secure cylinders to a cylinder cart, wall or stable work bench
Always keep cylinders secured properly in a vertical (up-right) position.
Do not drop, strike, or apply heat to any part of the cylinder or valve.
Notes: <number>
Securing the Cylinders

## Slide 4: Cylinder Protective Cap
Always keep the protective safety caps in place whenever cylinders are moved or are in storage (full or empty).
The cylinder cap has two holes on its sides:
Larger Oval Shaped Hole- designed to cause a cylinder with a broken-off valve to spin instead of taking-off like a missile.
Smaller Circular Hole- designed to make a loud whistling noise if the cylinder valve is broken-off, alerting the operator and others in the shop of danger.
Notes: <number>

## Slide 5: EMPTY CYLINDERS
Mark empty cylinders “EMPTY” or Place a ring around the protective cap.
Always close cylinder valves completely on empty cylinders.
Notes: <number>

## Slide 6: CRACKING THE CYLINDER VALVE
DO NOT stand directly in front of cylinder valve. Stand behind the cylinder valve while cracking and be aware of others in the shop, aiming in a safe direction.
Momentarily open and close the cylinder valve “cracking” - this will blow out any dust, dirt, or debris within the cylinder valve and prevent it from entering the regulator and seats.
Open the cylinder valve slightly. If the valve is opened too much the cylinder could tip over from the pressure.
If Acetylene cylinders spray a mist when cracked, let sit for 30 minutes allowing acetone to settle.
Notes: <number>

## Slide 7: Inspecting the Cylinder Valve and Regulator
Make sure the connection seat and threads on the cylinder valve are not damaged.
A damaged screw thread may ruin the regulator nut, while a poor connection seat will cause the gas to leak.
Carefully inspect the cylinder valves and regulator threads for traces of grease and oil. *If oil or grease is found DO NOT USE! Report to instructor immediately.

## Slide 8: ATTACHING THE REGULATOR
Connect the oxygen regulator to the oxygen cylinder and the acetylene regulator to the acetylene cylinder.
All Oxygen connections have right handed threads.
Oxygen cylinder valves have male fittings and the oxygen regulator have female fittings.
All Acetylene connections have left handed threads
Acetylene cylinder valves have female fittings and the Acetylene regulator have male fittings.
Notes: <number>

## Slide 9: Attaching the Regulator Cont.
Tighten regulators with a close-fitted wrench (open-end wrench). Do not use jawed tools such as pliers, vice grips or channel locks to tighten regulator nuts.
Do not over tighten regulators to cylinders. Fittings are made of Brass a soft metal and stripping will likely occur.
Make sure the regulator has the correct pressure rating for the cylinder being used.

## Slide 10: Turning on the Cylinder Valve
Never stand in front or behind a regulator when opening the cylinder valve. Always stand to the side of the cylinder leaving the cylinder between you and the regulator.
Be certain that the tension on the regulator adjusting screw is released. Unscrew adjusting screw counter clockwise until tension is removed.
Standing to the side of the cylinder, slowly open the oxygen cylinder valve until the maximum pressure registers on the high pressure gauge. Then open the oxygen cylinder valve all-the-way to seal the valve packing.
In the same manner, slowly open the acetylene cylinder valve. But only open the Acetylene valve ¾ - 1 full turn. Allowing the operator to quickly turn off the fuel in case of emergency.
Notes: <number>

## Slide 11: Adjusting the Oxygen Regulator *Never Exceed 40 PSI – Working Gauge
Working Gauge Cylinder Gauge
Oxygen Regulator Adjustment Screw
Oxygen Regulator- Female Fitting
Right Handed Threads
No Markings on nut
Notes: <number>

## Slide 12: Slowly Crack the Acetylene Cylinder Valve *Open cylinder valve ¾ - 1 full turn (quick shut-off)
Notes: <number>

## Slide 13: Adjusting the Acetylene Regulator *Never Exceed 15 PSI – Working Gauge
Working Gauge Cylinder Gauge
Acetylene Regulator - Adjustment Screw
Acetylene Regulator- Male Fitting
Acetylene Regulator- Left Handed Threads
Notches on Nut – Indicate Left Handed Threads.
Notes: <number>

## Slide 14: Oxy-Fuel Hoses
Oxygen Hoses- Are GREEN in color, have right-handed threads with no markings on the connecting nuts.
Acetylene Hoses- Are RED in color, have left handed threads, with notched markings on the connecting nuts.
New hoses should have the preservative talcum powder blown out before the welding or cutting torch is used.
Hoses are flame retardant, but should still be kept away from open flame, fallen slag, molten metal and sparks.
NEVER EXCEED 15 PSI ON THE ACETYLENE REGULATOR WORKING GUAGE.
NEVER EXCEED 40 PSI ON THE OXYGEN REGULATOR WORKING GUAGE
Notes: <number>