## Slide 1: Cutting Tip Chart
7. Refer to a cutting tip selection chart for correct cutting tip, regulator pressures, and travel speed.

## Slide 2: Lighting the Torch
8. Open the oxygen valve on the welding torch all the way.

## Slide 3: Lighting the Torch Cont.
Adjust the oxygen regulator to the desired delivery pressure.
DO NOT EXCEED 40 P.S.I.

## Slide 4: Lighting the Torch Cont.
Adjust the fuel (Acetylene) regulator delivery pressure.
DO NOT EXCEED 15 P.S.I.

## Slide 5: Lighting the Torch Cont.
11. Open the fuel valve on the torch handle approximately one-half turn and ignite the gas with a friction lighter (striker).
NOTE- Wear protective goggles or glasses (Shade #5) to shield the eyes from the bright light of the flame and leather gloves from potential burns when lighting the torch.

## Slide 6: Lighting the Torch Cont.
12. Continue to increase the fuel supply at the torch handle until the flame clears the end of the tip about 1/8”, then reduce the supply slightly to return the flame to the tip.

## Slide 7: Lighting the Torch Cont.
13. Slowly open the preheat oxygen control valve on the cutting attachment until the preheat flames establish a sharp inner cone (neutral flame).