## Slide 1: Shutting Down the Cutting Outfit
After the cutting operation is finished, or whenever the cutting torch operator must leave the work area, the oxy-acetylene cutting outfit must be shut down.

## Slide 2: Shutting Down the Cutting Outfit Step 1
Follow these procedures for shutting down the equipment:
Turn off the acetylene torch valve

## Slide 3: Shutting Down the Cutting Outfit Step 2
2. Turn off the oxygen torch valve

## Slide 4: Shutting Down the Cutting Outfit Step 3
3. Turn off the Acetylene cylinder valve.

## Slide 5: Shutting Down the Cutting Outfit Step 4
4. Turn off the Oxygen cylinder valve.

## Slide 6: Shutting Down the Cutting Outfit Steps 5 & 6
Reopen the acetylene torch valve and depress the oxygen cutting lever to release or bleed any gas still remaining in the hoses
When the regulators read zero - shut off the acetylene torch valve.

## Slide 7: Shutting Down the Cutting Outfit Step 7
7. Turn the oxygen and acetylene regulator adjusting screws counterclockwise until no tension remains (loose).

## Slide 8: Shutting Down the Cutting Outfit Step 8
8. Rewrap the Oxy-acetylene hoses on the outfit for proper clean-up and shop organization.