## Slide 1: Distance Measurement
Introduction
Distance is one of the most basic engineering measurements
Early measurements were made in terms of the dimensions of the body
Cubits - the distance between the tip of your middle finger to the elbow Typically to measure cords and textiles (another measure was 24 digits or 6 palms)

## Slide 2: Distance Measurement
Introduction
Fathom - distance between the tips of your middle finger when your arms are outstretched
The name comes from the Danish faedn, "outstretched arms."

## Slide 3: Distance Measurement
Introduction
Foot distance from the tip of a man’s big toe to the heel
Rod - the sum of the lengths of the left feet of 16 men (16.5 - 24 ft)

## Slide 4: Distance Measurement
Pacing
The ability to pace distance is very useful
A person can determine their pace by counting the number of paces necessary to walk a distance that has been previously measured
A pace is defined as one step
A stride is consider two steps or

## Slide 5: Distance Measurement
Pacing

## Slide 6: Distance Measurement
Measuring Wheels

## Slide 7: Distance Measurement
Taping or Chaining
For centuries engineers have measured distances with ropes, lines, or cords
The term chaining is a carry–over from the time when the Gunter chain was used (1600’s)
The 66 foot chain is made of 100 links 7.92 inches in length
In 1785 U.S. a federal law stated that all government surveys must be done with a Gunter's chain

## Slide 8: Distance Measurement
It lies at the origin of the definition of an acre.
The original acre was an area of land suitable for ploughing with a defined amount of work (e.g., ten furrows long, each furrow being ten chains, permitting rests of an oxen team)
It measured one chain by one furlong (totaling 10 square chains).
Early two–lane roads were laid out with a chain, resulting in a 66–ft right–of–way
Taping or Chaining

## Slide 9: Distance Measurement
Taping or Chaining

## Slide 10: Distance Measurement
Taping or Chaining
Tapes are available in lengths up to 1,000 feet; precision of 1/1,000 to 1/5,000 are commonly obtained

## Slide 11: Distance Measurement
Electronic Distance Measurement (EDM)
EDMs are very useful in measuring distances that are difficult to access or long distances

## Slide 12: Distance Measurement
Taping over Level Ground
If the taping is done over level ground where there is no underbrush, the tape can rest on the ground
A taping crew consists of two people: the head tapeperson and the rear tapeperson
The head tapeperson takes one end of the tape walks down the line towards the point
If the distance is more than 100–ft, then the head tapeperson places a taping pin at the 100–ft interval and the process is repeated

## Slide 13: Distance Measurement
Taping over Sloping Ground
If the taping is done over sloping ground where there is no underbrush, the taping must be done in sections, referred to as breaking the tape

## Slide 14: Distance Measurement
Taping over Sloping Ground
Holding the tape more than five feet above the ground is difficult, therefore slopes greater than 5 ft per 100 ft will require runs of less than 100 ft

## Slide 15: Distance Measurement
Taping over Sloping Ground
40 feet
35 feet
30 feet
Hold the tape level
Use a plumb bob to locate
the point
Height less than
5 feet

## Slide 16: Distance Measurements
End of Distance Measurements