## Slide 1: Differential Leveling
Importance of Leveling
  The determination of elevations is called leveling
  Measuring relative elevations changes is a comparatively simply process
  Precise and accurate control of relative elevations are critical to most construction projects

## Slide 2: Differential Leveling
The Level
  A level consist of a high-powered telescope
  The level is attached to a spirit or bubble level that keeps the line of sight of the telescope horizontal

## Slide 3: Differential Leveling
3. Level Instrument

## Slide 4: Differential Leveling
4.50
Level Instrument
4.60
4.55
4.51
4.52
4.53
4.54

## Slide 5: Differential Leveling
C. Definitions
Starting point
(elevation 100.00 ft)
Point A
Point B
BS = 6.32 ft
HI = 106.32 ft
FS = 3.10 ft
Elevation = 103.22 ft

## Slide 6: Differential Leveling
Definitions
1. Bench mark (BM) - relatively permanent point of known elevation
FS = 3.10 ft
Starting point
(elevation 100.00 ft)
Point A
Point B
BS = 6.32 ft
HI = 106.32 ft
FS = 3.10 ft
Elevation = 103.22 ft

## Slide 7: Differential Leveling
Definitions
2. Backsight (BS) - a sight taken to the level rod held at a point of known elevation (either a BM or TP)
Starting point
(elevation 100.00 ft)
Point A
Point B
BS = 6.32 ft
HI = 106.32 ft
FS = 3.10 ft
Elevation = 103.22 ft

## Slide 8: Differential Leveling
Definitions
3. Height of instrument (HI) - the elevation of the line of sight of the telescope
Starting point
(elevation 100.00 ft)
Point A
Point B
BS = 6.32 ft
HI = 106.32 ft
FS = 3.10 ft
Elevation = 103.22 ft

## Slide 9: Differential Leveling
Definitions
4. Foresight (FS) - a sight taken on any point to determine its elevation
Starting point
(elevation 100.00 ft)
Point A
Point B
BS = 6.32 ft
HI = 106.32 ft
FS = 3.10 ft
Elevation = 103.22 ft

## Slide 10: Differential Leveling
D. Computation of Elevations
Elevation 100.00
BS
12.64
Point
BM1
Elevation
BS
HI
FS
BM1
12.64
112.64
100.00
1. BS + Elevation = HI

## Slide 11: Differential Leveling
Computation of Elevations
Elevation 100.00
BS
12.64
FS
3.11
Point
BM1
TP1
Elevation
BS
HI
FS
TP1
BM1
12.64
112.64
3.11
109.53
2. HI - FS = Elevation
100.00

## Slide 12: Differential Leveling
Computation of Elevations
Elevation 100.00
BS
12.64
FS
3.11
Point
BM1
TP1
Elevation
BS
HI
FS
TP1
BM1
12.64
112.64
3.11
109.53
BS
10.88
10.88
120.41
100.00

## Slide 13: Differential Leveling
Computation of Elevations
Elevation 100.00
BS
12.64
FS
3.11
Point
BM1
TP1
Elevation
BS
HI
FS
TP1
BM1
12.64
112.64
3.11
109.53
BS
10.88
10.88
120.41
FS
2.56
TP2
2.56
TP2
117.85
100.00

## Slide 14: Differential Leveling
Computation of Elevations
Elevation 100.00
BS
12.64
FS
3.11
Point
BM1
TP1
Elevation
BS
HI
FS
TP1
BM1
12.64
112.64
3.11
109.53
BS
10.88
10.88
120.41
FS
2.56
TP2
2.56
TP2
117.85
BS
9.72
9.72
127.57
100.00

## Slide 15: Differential Leveling
Computation of Elevations
Elevation 100.00
BS
12.64
FS
3.11
Point
BM1
TP1
Elevation
BS
HI
FS
TP1
BM1
12.64
112.64
3.11
109.53
BS
10.88
10.88
120.41
FS
2.56
TP2
2.56
TP2
117.85
BS
9.72
9.72
127.57
BM2
FS
3.10
BM2
3.10
124.47
100.00

## Slide 16: Differential Leveling
Computation of Elevations
Elevation 100.00
BS
12.64
FS
3.11
Point
BM1
TP1
Elevation
BS
HI
FS
TP1
BM1
12.64
112.64
3.11
109.53
BS
10.88
10.88
120.41
FS
2.56
TP2
2.56
TP2
117.85
BS
9.72
9.72
127.57
BM2
FS
3.10
BM2
3.10
124.47
100.00

## Slide 17: Differential Leveling
Computation of Elevations
3. Change in elevation- summation of the backsight and the foresight then subtract
+33.24
-8.77
Change in elevation = 33.24 -8.77 =24.47
Point
BM1
TP1
Elevation
BS
HI
FS
12.64
112.64
3.11
109.53
10.88
120.41
2.56
TP2
117.85
9.72
127.57
BM2
3.10
124.47
100.00

## Slide 18: Differential Leveling
The initial backsight (BS) is taken to a point of known elevation
The backsight reading is added to the elevation of the known point to compute the height of the instrument (HI)
The level may be moved to a temporary point called a turning point (TP)
The elevation of a point is the height of the instrument (HI) minus the foresight (FS)

## Slide 19: Differential Leveling
Computation of Elevations - Group Problem
Prepare a set of level notes for the survey illustrated below. What are the elevations of points TP1 and TP2?
BS
1.27
FS
4.91
TP1
BM
BS
2.33
FS
6.17
TP2
Elevation 356.68

## Slide 20: Differential Leveling
Computation of Elevations - Group Problem
BS
1.27
FS
4.91
TP1
BM
BS
2.33
FS
6.17
TP2
Elevation 356.68
1.27
357.95
4.91
353.04
2.33
355.37
6.17
Point
BM1
TP1
Elevation
BS
HI
FS
TP2
349.20
356.68
+3.60
-11.08
-7.48

## Slide 21: Differential Leveling
Common Mistakes
  Misreading the rod - reading 3.54 instead of 3.45
  Moving the turning point - use a well–defined TP
  Field note mistakes - work within your group to check you records
  Mistakes with extended rod - make sure the leveling rod is fully extended

## Slide 22: Differential Leveling
Common Mistakes
Level rod not vertical
Settling of leveling rod
Leveling rod not fully extended or incorrect length
Level instrument not level
Instrument out of adjustment
Environment - wind and heat

## Slide 23: Differential Leveling
Suggestions for Good Leveling
Anchor tripod legs firmly
Check the bubble level before and after each reading
Take as little time as possible between BS and FS
Try to keep the distance to the BS and the FS equal
Provide the rodperson with a level for the rod

## Slide 24
Differential Leveling
End of Differential Leveling